## Slide 1
The Conventional
Computing Stack
From Human Problems to Electrons — Layer by Layer
A Deep Dive into How Computers Really Work

## Slide 2
THE FULL STACK — 9 LAYERS
1
Problem
Real-world challenge
2
Algorithm
Step-by-step logic
3
Program / Language
Code & syntax
4
System Software (OS)
Resource management
5
ISA
Software ↔ Hardware interface
6
Microarchitecture
CPU implementation
7
Logic (Digital Design)
Gates & circuits
8
Devices
Transistors & capacitors
9
Electrons
Voltage & physics
SOFTWARE
HARDWARE

## Slide 3
LAYERS 1 & 2: PROBLEM + ALGORITHM
Layer 1: Problem
The real-world challenge to solve
Human-centric — not technical yet
Examples: traffic prediction, AI model, banking system
Foundation for everything below
Layer 2: Algorithm
Converts problem into logical steps
Language & hardware agnostic
Examples: sorting, searching, ML training
Foundation for efficient computation

## Slide 4
LAYERS 3 & 4: PROGRAM / LANGUAGE + SYSTEM SOFTWARE
Layer 3: Program / Language
Algorithms implemented in code (Python, C++, Java)
Compiled or interpreted into machine form
Introduces syntax, data structures, libraries
Bridges human logic and machine execution
Layer 4: System Software
Operating System (Windows, Linux, macOS)
Memory management & process scheduling
Virtual machines provide abstraction
Bridge between software and hardware

## Slide 5
LAYER 5: ISA — THE CRITICAL BRIDGE
Instruction Set Architecture
"The language the CPU understands"
What it Defines
ADD, LOAD, STORE instructions
Registers & data types
Memory addressing modes
Key Examples
x86 — Intel & AMD desktop/server
ARM — Mobile & Apple Silicon
RISC-V — Open-source ISA
Why It Matters
Decouples SW from HW impl.
Same ISA → code portability
Bridge in the full stack

## Slide 6
LAYERS 6 & 7: MICROARCHITECTURE + LOGIC
Layer 6: Microarchitecture
The physical implementation of ISA
Includes pipelines, caches (L1/L2/L3)
Branch prediction & out-of-order execution
Same ISA, different perf = different microarch
Layer 7: Logic / Digital Design
Built using logic gates: AND, OR, NOT
Forms adders, multiplexers, control units
Implemented via digital circuits on chip
Where software logic becomes electrical

## Slide 7
LAYERS 8 & 9: DEVICES + ELECTRONS
Layer 8: Devices
Physical components: transistors & capacitors
Implement logic gates in silicon
Modern CPUs hold billions of transistors
Built at nanometre scale (3–5 nm today)
Layer 9: Electrons
The lowest physical layer
Voltage levels represent 0 and 1 (binary)
Governed by physics
All computation reduces to electron flow

## Slide 8
COMPUTING STACK — LAYER 8 & 9
Semiconductors
& Doping
How silicon becomes a switch — the physics behind every transistor
~1nm
Gate length (TSMC 3nm)
50B+
Transistors per chip
1.1 eV
Silicon band gap

## Slide 9
WHAT IS A SEMICONDUCTOR?
Electrical Conductivity Spectrum
Insulator
Glass, Rubber
Semiconductor
Silicon, Germanium
Conductor
Copper, Gold
← Low conductivity
High conductivity →
Controllable
Conductivity can be switched on/off with voltage or heat — perfect for transistors.
Silicon (Si)
4 valence electrons. Forms a stable crystal lattice. Most abundant semiconductor element.
Band Gap
Energy gap between valence & conduction bands. Silicon's 1.1 eV gap enables room-temperature switching.

## Slide 10
DOPING — ENGINEERING CONDUCTIVITY
Doping = intentionally adding impurity atoms to pure silicon to control electron flow
N-TYPE
Si
Si
Si
Si
Si
P
Si
Si
Si
Si
Si
Si
e⁻
Dopant: Phosphorus (P) or Arsenic (As)
5 valence electrons — 1 extra electron donated
Majority carriers: FREE ELECTRONS (negative)
Current flows easily when voltage applied
P-TYPE
Si
Si
Si
Si
Si
B
Si
Si
Si
Si
Si
Si
h⁺
Dopant: Boron (B) or Gallium (Ga)
3 valence electrons — creates an electron hole
Majority carriers: HOLES (positive charge)
Holes move as electrons fill adjacent gaps

## Slide 11
FROM DOPING → TRANSISTORS → CHIPS → COMPUTATION
1
Pure Silicon
Refined to 99.9999999%
purity (9N grade)
→
2
Doping
Phosphorus (N) &
Boron (P) implanted
→
3
P-N Junctions
Diodes, enabling
one-way flow
4
MOSFET
Gate controls
channel ON/OFF
→
5
Logic Gate
NAND/NOR from
2-4 transistors
→
6
CPU / Chip
50B+ transistors
3–5nm node
→ This chain maps directly to Layers 8–9 (Devices & Electrons) of the Computing Stack

## Slide 12
KEY TAKEAWAYS
What makes the computing stack powerful
01
Abstraction at Every Layer
Each layer hides complexity from the one above. Programmers never need to think about electrons; hardware engineers don't need to worry about algorithms.
02
ISA is the Critical Seam
The Instruction Set Architecture is where software meets hardware. It enables code portability across different physical implementations.
03
Same ISA, Different Performance
Two CPUs sharing an ISA (e.g. x86) can vary enormously in speed — all due to microarchitecture: pipelines, caches, and branch prediction.
04
Everything is 0s and 1s
At the lowest level, all computation reduces to voltage levels — high or low — governed by the physics of electron movement in silicon.